# www.cnstrongpower.net

橡胶线中国生产厂家,供应商,工厂

美国UL橡胶线 | 日本PSE JET橡胶线 | 欧洲VDE 中国CCC橡胶线 |

| Type | Conductor | Insulation Thickness | Jacket Thickness | Overall Diameter | Min.Cross-sectional area of Conductor |
| --- | --- | --- | --- | --- | --- |
|  | [mm] | [mm] | [mm] | [mm2] |
| Size | No./mm |  |  |  |  |
| SV | 18AWG/2C | 41/0.160 | 0.38 | 0.76 | 5.60±0.10 | 0.798 |
| SV0 | 17AWG/2C | 52/0.160 | 5.90±0.10 | 1.01 |
| SV00 | 16AWG/2C | 65/0.160 | 6.20±0.10 | 1.27 |
|  | 18AWG/3C | 41/0.160 | 5.90±0.10 | 0.798 |
|  | 17AWG/3C | 52/0.160 | 6.20±0.10 | 1.01 |
|  | 16AWG/3C | 65/0.160 | 6.60±0.10 | 1.27 |

| Type | Conductor | Insulation Thickness | Jacket Thickness | Overall Diameter | Min.Cross-sectional area of Conductor |
| --- | --- | --- | --- | --- | --- |
| Size | No/mm | [mm] | [mm] | [mm] | [mm2] |
| S | 18AWG/2C | 41/0.160 | 0.76 | 1.52 | 8.60±0.15 | 0.798 |
| SO | 16AWG/2C | 65/0.160 | 0.76 | 1.52 | 9.20±0.15 | 1.27 |
| SOO | 14AWG/2C | 41/0.254 | 1.14 | 2.03 | 12.5±0.20 | 2.02 |
| SOW | 18AWG/3C | 41/0.160 | 0.76 | 1.52 | 9.00±0.15 | 0.798 |
| SOOW | 16AWG/3C | 65/0.160 | 0.76 | 1.52 | 9.70±0.15 | 1.27 |
|  | 14AWG/3C | 41/0.254 | 1.14 | 2.03 | 13.2±0.20 | 2.02 |
|  | 18AWG/4C | 41/0.160 | 0.76 | 1.52 | 9.70±0.15 | 0.798 |
|  | 16AWG/4C | 65/0.160 | 0.76 | 1.52 | 10.5±0.20 | 1.27 |
|  | 14AWG/4C | 41/0.254 | 1.14 | 2.03 | 14.2±0.20 | 2.02 |
|  | 18AWG/5C | 41/0.160 | 0.76 | 2.03 | 11.5±0.20 | 0.798 |
|  | 16AWG/5C | 65/0.160 | 0.76 | 2.03 | 12.4±0.20 | 1.27 |
|  | 14AWG/5C | 41/0.254 | 1.14 | 2.41 | 16.2±0.20 | 2.02 |

| TYPE | Conductor | Insulation | Green Grounding Cond. | Overall Diam | Max.Cond.Resist. |
| --- | --- | --- | --- | --- | --- |
|  | [mm] | ohm/km/20 |
| AWG | Construction | Nom.thick.[mm] | Nom.Thick. | Nom.Thick. |  |  |
| [NO./mm] |  | mm | [mm] |  |  |
| HPN | 16/2C | 65/0.16 | 1.14 | - | - | 3.9±0.05x7.6±0.10 | 13.7 |
| 18/2C | 41/0.16 | 1.14 | 3.5±0.05x6.9±0.10 | 21.8 |
| 16/3C | 65/0.16 | 1.14 | 0.38 | 0.33 | 3.9±0.05x10±0.15 | 13.7 |
| 18/3C | 41/0.16 | 1.14 | 3.5±0.05x9.0±0.15 | 21.8 |
| 17/2C | 52/0.16 | 1.14 | - | - | 3.7±0.05x7.2±0.20 | 17.2 |
| 14/2C | 41/0.254 | 2.03 | 6.0±0.1x10.7±0.15 | 8.62 |
| 14/3C | 41/0.254 | 2.03 | 0.38 | 0.33 | 6.0±0.1x12.6±0.15 | 8.62 |

美国UL电源线 | 欧洲VDE电源线 | 澳大利亚SAA电源线 | 英国BSI 1363 A电源线 | 韩国KSC电源线 | 日本PSE JET电源线 | 意大利IMQ电源线 | 南非SABS电源线 | 瑞士SEV电源线 | 阿根廷IRAM电源线 | 巴西UC电源线 | 以色列SII电源线 | 丹麦标准电源线 | 中国CCC电源线 |IEC 60320连接器电源线 |自锁电源线|干燥器电源线|工业插头电源线|延长线|橡胶线|PVC塑料电源线|拖线板|开瓶器|电源线镀锌扎丝|饺子器|切菜器

宁波云环电子集团有限公司(Strong Power Electronics CORP)

地址: 浙江省余姚市泗门镇小路下,315472

电话: 0086-574-62164180

传真 0086-574-62160100

手机: 15867340789

联系人: 邵洪波先生

邮箱 sales@powercordchina.com

网址: http://www.cnstrongpower.net 电源线,电源线插头,插头线,延长线,iec电源线,ul电源线,欧洲vde ce rohs电源线, 日本pse jet 英国bsi电源线,饺子器,电源线镀锌绝缘扎丝,开瓶器,切菜器,宁波云环程隆电器